## Slide 1: Project name: Interdigitated Electrodes in Microfluidics Team members: Erin Ingram & Omar Mahmood
Notes: Erin

## Slide 2: Crash Course: Droplet Microfluidics
Perform high precision biological experiments on the scale of 𝜇m
“Lab on a chip”
Uniform droplets essential to precision – want to trap single cells, DNA molecules, etc. in one droplet
Notes: Erin

## Slide 3: Problem Statement
Satellite droplets form during droplet generation and negatively affect the manipulation of desired droplets due to cross contamination, leading to false test results
Notes: Omar

## Slide 4: Satellite droplet formation
Notes: Omar

## Slide 5: Our solution
Design a two stage filtration system incorporating an Interdigitated Electrode (IDE) arrays to perform size based filtration and prevent satellite droplets from making it to the chip’s output
Fabricate entire device in AggieFab – nano/micro fabrication facility
Fluid flow
Electrodes
Notes: Erin

## Slide 6: Task partition
Omar: Stage 1 high-pass filter
Erin: Stage 2 band-pass filter
Our research:
  Experiment with different IDE designs
  Manipulate parameters: finger width, distance, voltage applied
  Never been done before
  First trials: 5 𝜇m width and 5 𝜇m distance, 10 and 10, 20 and 20
Notes: Both

## Slide 7: Why two stages?
Uniform droplets are needed for input to the PCR equipment, in order to trap single DNA molecules in single droplets
Temperature changes during PCR process can affect droplet size – lead to splitting and merging
Notes: Erin

## Slide 8: Subsystems and Interface
Droplet
Channel - Fabricated by Omar
IDE- Fabricated by Omar
Satellite droplets - “waste”
Desired droplets
Various droplet sizes
IDE - Fabricated by Erin
1
2
3
1- Droplets not big enough - “Waste”
2- Droplets too big - “Waste”
3- Perfect size
Final Droplets
Satellite droplet
PCR
Channel - Fabricated by Erin
Notes: Both

## Slide 9: Our lab-on-a-chip design
Notes: Both

## Slide 10: IDE Design
Solder to voltage source
Notes: Omar

## Slide 11: Plan
9/16/22 | 9/30/22 | 10/14/22 | 10/28/22 | 11/11/22 | 11/25/22
Train on non-cleanroom related tasks: -PDMS/Soft-lithography -Plasma cleaner -Microscopes -PCR techniques | Design the channel, fabricate master mold using NanoScribe | Design the IDE, train on metal deposition and wet etching | Finish fabrication of the channel and the IDE, plasma bond IDE onto channel | Perform experiments using the bonded device, experiment with different IDE characteristics, compare simulation results with experimental | Test using ideal IDE parameters
***Both team members follow the same schedule for their specific subsystem
Notes: Erin